## Slide 1: Tides
and Navigation
©Navigational Algorithms

## Slide 3: The importance of monitoring the Tides and their Currents
For what?
Beach?
Avoid embarrassing situations, such as a grounding

## Slide 8: Gravitational forces and rotation of Earth
h = f( G*m1*m2 /d2)
Moon:Sun = 34:15
La Luna  2T = 24:50
El Sol  2T = 24:00
Otros planetas
h = f( cos B )

## Slide 9: Effects of the declination of the Moon

## Slide 10: Effects of the declination of the Moon

## Slide 11: Effects of the declination of the Moon

## Slide 12: Tides and phase of the Moon
Spring tides occur at times of new and full Moon. Range of tide is greater than average since solar and lunar tractive forces act in same direction.
(B) Neap ties occur at times of first and third quarters. Range of tide is less than average since solar and lunar tractive forces act at right angles.
Mareas vivas ó sizigias
Edad = 0 días -> Luna nueva
Edad = 14.75 días -> Luna llena
Mareas muertas ó de cuadratura
Edad = 7 días -> Cuarto creciente
Edad = 21 días -> Cuarto menguante

## Slide 13: Tides and phase of the Moon

## Slide 15: What Else Affects Tides?
The shape of bays and estuaries, geographic location and weather patterns all can affect local tidal intensity.
The relative distances and positions of the sun, moon and Earth all affect the size and magnitude of the Earth’s two tidal bulges. At a smaller scale, the magnitude of tides can be strongly influenced by the shape of the shoreline. When oceanic tidal bulges hit wide continental margins, the height of the tides can be magnified. Conversely, mid-oceanic islands not near continental margins typically experience very small tides of 1 meter or less.
The shape of bays and estuaries also can magnify the intensity of tides. Funnel-shaped bays in particular can dramatically alter tidal magnitude. The Bay of Fundy in Nova Scotia is the classic example of this effect, and has the highest tides in the world – over 15 meters. Narrow inlets and shallow water also tend to dissipate incoming tides. Inland bays such as Laguna Madre, Texas, and Pamlico Sound, North Carolina, have areas classified as non-tidal even though they have ocean inlets. In estuaries with strong tidal rivers, such as the Delaware River and Columbia River, powerful seasonal river flows in the spring can severely alter or mask the incoming tide.
Local wind and weather patterns also can affect tides. Strong offshore winds can move water away from coastlines, exaggerating low tide exposures. Onshore winds may act to pile up water onto the shoreline, virtually eliminating low tide exposures. High – pressure systems can depress sea levels, leading to clear sunny days with exceptionally low tides. Conversely, low-pressure systems that contribute to cloudy, rainy conditions typically are associated with tides than are much higher than predicted.

## Slide 17: Types of Tide – Continental Interference

## Slide 18: Heights of tide
Amphidromic point
Los puntos anfidrómicos se producen debido al efecto de Coriolis y la interferencia dentro de las cuencas oceánicas, los mares y las bahías creando un patrón de onda - llamado sistema anfidrómico

## Slide 19: Heights of tide

## Slide 20: Theory of tides
Tidal Harmonic constituent
Higher harmonics
  M4 Shallow water overtides of principal lunar
  M6 Shallow water overtides of principal lunar
  MK3 Shallow water terdiurnal
  S4 Shallow water overtides of principal solar
  MN4 Shallow water quarter diurnal
  Mareógrafo Socoa

## Slide 22: Tides and Navigation

## Slide 23: Heights of tide
Variations in the ranges and heights of tide where the chart sounding datum is Indian Spring Low Water.

## Slide 24: Tide interpolator

## Slide 25: Interpolation problems

## Slide 26: Online prediction

## Slide 27
Thank you so much for your time and attention
ESKERRIK ASKO
https://sites.google.com/site/navigationalalgorithms/