## Slide 1: Aircraft Celestial Navigation Intro By Michael Jones
You are heading for home on March 16th, 2020.
No VOR and the Battery just died on your handy GPS
But you do have your trusty sextant, watch, Almanac, and Pub 249.
Notes: A basic intro to celestial navigation. A 3 star running fix.

## Slide 2
This is your dead reckoning plot.
You are flying directly westbound heading for home on March 16th (03/17/20 at 02:45z)
TC 270°
150 Kts
DR 02:48Z
Notes: Dr, 270° at 150 Kts.

## Slide 3
DR 03:00Z
TC 270°
150 Kts
DR 02:48Z

## Slide 4
Wind 340° @ 15kt
Actual Position
At 03:04z
will be here
It has been several hours since your last fix.
Your Flight has been uneventful. but a wind from 340° at 15 Kts has shifted your track for the last 2 hours.
Actual Track 264° / 145kt
TC 270°
150 Kts
DR 02:48Z
Notes: Wind for the past two hours has affected your track. The blue line is your actual track. Red is the two hour wind vector.

## Slide 5
Wind 340° @ 15kt
We will plan three star sights at 4 minute (10 Nm) intervals
02:52Z 02:56Z and 03:00Z
This makes use of the Almanac and tables easier.
TC 270°
150 Kts
DR 02:48Z
Notes: Plan a three star fix at 03:04Z March 17, 2020. Sights at 02:52, 02:56, and 03:00.

## Slide 6
These are the books we need to use
Celestial Navigation.

## Slide 7: Bubble Sextant
A-12 Sextant
A-8 Sextant
Notes: Typical aviation sextants.

## Slide 8
Aries GHA:
02:50Z, 217° 38.6’
03:00Z, 220° 09.0’
Z
From the 2020 Air Almanac
Interpolation Table is in
The front of the Almanac
Notes: Get the Global Hour Angle of Aries. Aries is an arbitrary starting point locations of heavenly bodies.

## Slide 9
Dead Reckoning
Information
Notes: Precomputation sheet.

## Slide 10
Pub 249
Vol. 1
Selected Stars
Notes: HO-249 Vol 1. Find assumed latitude page (44°N), Find Local hour angles (131, 132, 133), and pick out 3 stars for the sights. Stars marked with a diamond are ideally spaced for a three star fix. Note the computed height and zenith angle for each star on the precomputation sheet. Now we have information to take star

## Slide 11
Notes: Precomputation sheet.

## Slide 12
Sextant
Angles (Sights)
Notes: Now we are ready to take our sextant sights. I did this in a planetarium program called Stellarium so these sight are an ideal. Most aircraft fixes are considered good if there is a five mile accuracy.

## Slide 13: “Sights” by Stellarium Planetarium Program.
A free planetarium program. https://stellarium.org/
Aldebaran:
Ho 31° 27’
Az 263° (confirms computed Zn 263°
The other star “sights” were done in similar fashion.
Notes: “

## Slide 14
Assumed
Point (AP)
Aldebaran 263° 12 nm
Away From AP
DR 02:52Z
TC 270°
150 Kts
Notes: First sight, Aldebaran. Line of Position is red line. We are somewhere along this line.

## Slide 15
Assumed
Point (AP)
Aldebaran 263° 9 nm
Away From AP
DR 02:52Z
Actual Location
43°20’N 86°44’W
TC 270°
150 Kts
Notes: I paused the time and added our other two stars to show you where we actually are on the map.

## Slide 16
Assumed
Point (AP)
DR 02:56Z
Regulus 145° 37 nm
Toward Star
TC 270°
150 Kts
Notes: Next star, Regulus. We are somewhere along the red LOP.

## Slide 17
Assumed
Point (AP)
DR 02:56Z
Actual Location
43°19’N 86°59’W
Regulus 145° 37 nm
Toward Star
TC 270°
150 Kts
Notes: Again, time paused and the other two stars added.

## Slide 18
Assumed
Point (AP)
DR 03:00Z
Kochab 22° 40nm
Away from AP
TC 270°
150 Kts
Notes: Third star sight, Kochab.

## Slide 19
DR 03:00Z
Actual Location
43°18’N 87°12’W
Kochab 22° 40nm
Away from AP
TC 270°
150 Kts
Notes: We are here.

## Slide 20
FIX 03:04Z
DR 03:00Z
Actual Location
43°18’N 87°27’W
TC 270°
150 Kts
Notes: This is the way our map looks after the three sights, and without any correction for the different times the sights were added. The sights are 4, 8, and 12 minutes early, so we advance each sight along our dead reckoning track by their respective times. 150 kts is 10 miles every four minutes, Aldebaran is advanced 30 miles at 270°, Regulus 20 miles at 270°, and kochab 10 miles at 270°. Note you would actually advance your assumed point by it’s respective time when you draw your star sights I did this to demonstrate the result.

## Slide 22: Resources for this Presentation
Maps: https://skyvector.com/
Free Planetarium: https://stellarium.org/
2020 Air Almanac: http://fer3.com/arc/imgx/aira20_all.pdf
HO-249 Volume 1: https://www.celestaire.com/download/pub-249-volume-1/
HO-249 Volume 2: https://www.celestaire.com/download/pub-249-volume-2/
HO-249 Volume 3: https://www.celestaire.com/download/pub-249-volume-3/